## Slide 1: Team Details
Case Study No.

## Slide 2
A small classifier tells CAKE which flow is the call
So calls and games stay usable when they share a device with downloads, where fair queueing and threshold rules both fail
Interim: 6 of 10 seeds, emulated
One laptop
a video call + 10 file-sharing connections
1/11
of the laptop's share is all fair queueing gives the call
Threshold rules: over 200 packets/s means Bulk, and HD calls send 400 to 600
89% qosify 0% ours
of cloud-game flows sent to Bulk
LightGBM
7 classes
1.4 ms
First 8 packets
sizes and gaps, no payload
94% accuracy 0.74 macro-F1
on 3,607 held-out flows. Video calls 100%, games 95% found
Voice
Video
Best Effort
Bulk
CAKE's four tins
the call
file sharing
Least harm
lowest expected damage, then a safety shield
87%
less damage than plain CAKE
flows left unusable over 9 home scenarios, 5.58 down to 0.73
Chart: 
| Ours, full system | Ours, simple rule | Threshold rules | Plain CAKE | No QoS
Flows left unusable | 0.73 | 1.65 | 6.91 | 5.58 | 12.31
94% → 2%
late frames on the HD call
while its laptop shares files. Median of 6 seeds; the chart is one run, sharing starts at 30 s
Chart: 
Call +
download
Line
drops
TVs +
console
Game +
backup
Busy
evening
Call +
file sharing
Game +
update
Flows
change
Controller
killed
Wins where a call or game shares its device with bulk traffic or the line speed changes. Ties where plain CAKE already copes
53 of 54
runs equal or better than plain CAKE. 0 worse than threshold rules
Line drop 100 to 20 Mbit/s caught in 353 ms · Watchdog back to plain CAKE in 2.02 s (limit 3 s) · QoE check rolls back bad changes · 214 unit tests
Interim: 6 of 10 seeds. 270 of 270 runs valid in an emulated home testbed on Linux CAKE; rootless, one command to reproduce; not yet on router hardware
How it works, in full
LINK_TBD